## Slide 1
Main page
Date Time Log level Log details
23.06.2023 6:15 error A, sensor 3, solenoid 3, mode real, attempt 2, 1% humidity, 2 category
23.06.2023 6:16 warning A, sensor 3, solenoid 3, switched to model
25.06.2023 6:00 fatal connection with device is failure
Plants connected to the system
Plant Sensor Solenoid Mode Category Included in irrigation
Petunia 1 1 real 6 Yes
Rose 2 2 real 8 Yes
Lavender 3 3 model 2 Yes
Delphinium 4 4 real 6 Yes
Tulip 6 6 real 5 No
Last warnings & errors
Automatic mode

## Slide 2
Connection/disconnection to/from the system
Date Time Sensor Solenoid Pin Operation Report
23.06.2023 16:00 5 5 27 Connection Success
23.06.2023 16:12 1 1 17 Disconnection Success
Connect new plant
Disconnect
# of flowerpot to disconnect
plant name
plant moisture category
choose one from available pins
# of solenoid

## Slide 3
Manual control
Check/uncheck all
Flowerpot 4
Flowerpot 3
Flowerpot 2
Flowerpot 1
Run one manual irrigation
Check humidity
Switch to real mode
Exclude from irrigation
Date Time Sensor Solenoid Operation Report
23.06.2023 16:00 1 1 Check humidity 34%
23.06.2023 16:02 1 1 Check humidity 100%
23.06.2023 16:12 1 1 Switch to real mode Success
23.06.2023 16:13 1 1 Switch to real mode Already done
It possible to check manually if sensor is alive…
… and return to real mode if it is
Manual sprinkling one and only time, auto control will be kept for the next times
Next times selected flowerpots will not be irrigated
Include to irrigation

## Slide 4
Date Time Log level Log details
23.06.2023 6:00 info A, sensor 1, solenoid 1, mode real, attempt 1, 5% humidity, 6 category, duration 20s
23.06.2023 6:00 info A, sensor 2, solenoid 2, mode real, attempt 1, 5% humidity, 8 category, duration 20s
23.06.2023 6:00 info A, sensor 3, solenoid 3, mode real, attempt 1, 10% humidity, 2 category, duration 20s
23.06.2023 6:00 info A, sensor 4, solenoid 4, mode model, attempt 1, __% humidity, 6 category, duration 20s
23.06.2023 6:15 info A, sensor 1, solenoid 1, mode real, attempt 2, 60% humidity, 6 category, duration 15s
23.06.2023 6:15 info A, sensor 2, solenoid 2, mode real, attempt 2, 75% humidity, 8 category, duration 15s 23.06.2023 6:15 error A, sensor 3, solenoid 3, mode real, attempt 2, 1% humidity, 2 category
23.06.2023 6:16 warning A, sensor 3, solenoid 3, switched to model
23.06.2023 6:16 info A, sensor 3, solenoid 3, mode model, attempt 3, __% humidity, 6 category, duration 10s
23.06.2023 6:20 info A, sensor 1, solenoid 1, mode real, attempt 4, 100% humidity, 6 category, -
23.06.2023 6:20 info A, sensor 2, solenoid 2, mode real, attempt 4, 100% humidity, 8 category, -
23.06.2023 6:20 info A, sensor 3, solenoid 3, mode model, attempt 4, __% humidity, 2 category, duration 2s
23.06.2023 6:20 info A, sensor 4, solenoid 4, mode model, attempt 4, __% humidity, 6 category, duration 8s
------------------------------------------------------------------------------------------------------------------------------------------------------------------
24.06.2023 6:00 info A, sensor 1, solenoid 1, mode real, attempt 1, 35% humidity, 6 category, duration 20s
24.06.2023 6:00 info A, sensor 2, solenoid 2, mode real, attempt 1, 45% humidity, 8 category, duration 20s
24.06.2023 6:00 info A, sensor 3, solenoid 3, mode model, attempt 1, __% humidity, 2 category, duration 2s
24.06.2023 6:00 info A, sensor 4, solenoid 4, mode model, attempt 1, __% humidity, 6 category, duration 20s
24.06.2023 6:15 info A, sensor 1, solenoid 1, mode real, attempt 2, 100% humidity, 6 category, -
24.06.2023 6:15 info A, sensor 2, solenoid 2, mode real, attempt 2, 100% humidity, 8 category, -
24.06.2023 6:15 info A, sensor 3, solenoid 3, mode model, attempt 2, __% humidity, 2 category, -
24.06.2023 6:15 info A, sensor 4, solenoid 4, mode model, attempt 2, __% humidity, 6 category, duration 5s
------------------------------------------------------------------------------------------------------------------------------------------------------------------
25.06.2023 6:00 fatal connection with device is failure
Logs
From …
Show
… till
Log level

## Slide 5
GPIO
Raspberry Pi4
NAT
FreeBox
WiFi (LAN)
Browser
(WAN)
Eau
Pompe
interrupteurs reed
Capteur d'humidité
< Solénoïdes >
Capteur d'humidité
Capteur d'humidité

## Slide 6
Device control
WebServer
Base de données
Driver de la pompe
Driver de capteurs
Driver de solénoïdes
AppServer
Hardware - GPIO

## Slide 7
GPIO
Raspberry Pi4
NAT
FreeBox
WiFi (LAN)
Browser
(WAN)
Relay board
…

## Slide 8
a/m Date Time Sensor Solenoid Mode Attempt Log level Details Duration
A 23.06.2023 6:00 1 1 real 1 info 5% humidity, 6 category 20
A 23.06.2023 6:00 2 2 real 1 info 5% humidity, 8 category 20
A 23.06.2023 6:00 3 3 real 1 info 10% humidity, 2 category 20
A 23.06.2023 6:00 4 4 model 1 info __% humidity, 6 category 20
A 23.06.2023 6:15 1 1 real 2 info 60% humidity, 6 category 15
A 23.06.2023 6:15 2 2 real 2 info 75% humidity, 8 category 15
A 23.06.2023 6:15 3 3 real 2 error 1% humidity, 2 category
A 23.06.2023 6:16 3 3 warning switched to model
A 23.06.2023 6:16 3 3 model 3 info __% humidity, 6 category 10
A 23.06.2023 6:00 1 1 real 4 info 100% humidity, 6 category -
A 23.06.2023 6:00 2 2 real 4 info 100% humidity, 8 category -
A 23.06.2023 6:00 3 3 model 4 info __% humidity, 2 category 7
A 23.06.2023 6:00 4 4 model 4 info __% humidity, 6 category 8
------------------------------------------------------------------------------------------------------------------------------------------------------------------
A 24.06.2023 6:00 1 1 real 1 info 35% humidity, 6 category 20
A 24.06.2023 6:00 2 2 real 1 info 45% humidity, 8 category 20
A 24.06.2023 6:00 3 3 model 1 info __% humidity, 2 category 20
A 24.06.2023 6:00 4 4 model 1 info __% humidity, 6 category 20
A 24.06.2023 6:15 1 1 real 2 info 100% humidity, 6 category -
A 24.06.2023 6:15 2 2 real 2 info 100% humidity, 8 category -
A 24.06.2023 6:15 3 3 model 2 info __% humidity, 2 category 5
A 24.06.2023 6:15 4 4 model 2 info __% humidity, 6 category 5
------------------------------------------------------------------------------------------------------------------------------------------------------------------
A 25.06.2023 6:00 fatal connection with device is failure
Logs
From …
Show
… till
Log level